## Slide 1
Submitted By:
S.SRINIDHI R.M. RAMYA
Bluejacking

## Slide 2: Content
Introduction
Bluejacking Technology
Architecture
Technical Features
How to Bluejack
Usage of bluejacking
Related concepts
Future aspects
Conclusion
Reference

## Slide 3: Introduction
Bluejacking
  Sending of unsolicited messages over Bluetooth to Bluetooth-enabled devices such as mobile phones, PDAs or laptop computers via the OBEX protocol.
Origin
  Started after a Malaysian IT consultant named “Ajack” posted a comment on a mobile phone forum.

## Slide 4: Bluejacking Technology
Bluetooth technology
vCard
OBEX protocol

## Slide 5: Architecture
Piconet
The devices find each other and form a network called “ piconet ” spontaneously.
A piconet is a basic unit with up to 8 nodes, one of which is a master and up to seven active slave nodes within a maximum distance of 10 meters.
All communication between master and slaves.
Piconet is a centralized TDM system.
Master controls clock and decides the time slot for the device.
In a piconet , there can be up to 255 parked nodes.
Master switches to low power state and parked node wait for beacon from master.

## Slide 7: Technical Features
Connection Type | Spread Spectrum (Frequency Hopping) & Time Division Duplex (1600 hops/sec)
Spectrum | 2.4 GHz ISM Open Band (79 MHz of spectrum = 79 channels)
Modulation | Gaussian Frequency Shift Keying
Transmission Power | 1 mw – 100 mw
Data Rate | 1 Mbps
Range | 30 ft
Supported Stations | 8 devices
Data Security –Authentication Key | 128 bit key
Data Security –Encryption Key | 8-128 bits (configurable)
Module size | 9 x 9 mm

## Slide 8: Classification
Classification of devices on the basis of Power dissipated & corresponding maximum Range.
 | POWER | RANGE
CLASS I | 20 dBm | 100 m
CLASS II | 0-4 dBm | 10 m
CLASS III | 0 dBm | 1 m

## Slide 9: How to Bluejack
Mobile
Personal computers
Software tools
  Bluespam
    Searches for all discoverable Bluetooth devices and sends a file to them (spam's them) if they support OBEX.
    By default a small text will be send.

## Slide 10: Usage of bluejacking
Busy shopping centre
Starbucks
Train Station
High Street
On a train/ tube/ bus
Cinema
Café/ restaurant/ pub
Mobile phone shop
Electronics shop (e.g. Dixons)

## Slide 11: Places where bluejack occurs
Chart: 
| Public transportation | Stores ans shopping malls | Restaurants | Bars | Cafés | Home
Places where bluejack occures | 23.4 | 32.1 | 9.8 | 11.2 | 7.3 | 0.7

## Slide 12: Related concepts
Bluesnarfing
Bluebugging

## Slide 13: Bluesnarfing
Is the unauthorized access of information from a wireless device through a Bluetooth connection, often between phones, desktops, laptops, and PDAs.
Even if your device is hidden bluesnarfing can also be done.

## Slide 14: Bluebugging
Form of Bluetooth attack.
Allows the user to take control of a victim's phone to call the user's phone.

## Slide 15: Counters-measures
Turn off your Bluetooth device until you need to communicate with another user.
Buy an E2X bag.
  It blocks all transmissions and receiving signals from leaving the bag.

## Slide 16: Conclusion
Because of its low cost and power consumption this technology has a great future ahead.

## Slide 17: Reference
www.google.com
www.wikipedia.com
www.studymafia.org

## Slide 18
Thanks